Supporting Information

Table S1: Densities, ρ of pure components at T= 298.15 K and pressure p = 0.1 MPa

| Chemical Name | (g·cm–3) |
| --- | --- |
|  | expt. | lit. |
| Aniline | 1.0167 | 1.01744 a |
| 1-pentanol | 0.8108 | 0.81073b |
| 1-hexanol | 0.8151 | 0.8148 c |
| 1-heptanol | 0.8187 | 0.81879 d |
| 1-octanol | 0.8214 | 0.82181 e |
| 1-nonanol | 0.8240 | 0.82448 f |
| 1-decanol | 0.8261 | 0.8265 g |

a Ref  13.  b Ref  14.   c  Ref  15.   d  Ref  16.   e  Ref  17.   f  Ref  18.   g  Ref  19.

Standard uncertainties are u(T) = 0.02 K, u(x) = 0.001, u(p) = 10 kPa, expanded uncertainty for density is U(ρ) = 0.001 g·cm-3

Table S2.  Experimental properties of pure compounds at T = 298.15 K needed for the application of the Kirkwood–Buff formalism. a

| Compound | ( cm–3.mol-1) | 104(K-1) | (M.Pa-1) |
| --- | --- | --- | --- |
| Aniline | 91.6 | 863 | 731 |
| 1-Pentanol | 108.7 | 916 | 884 |
| 1-Hexanol | 125.3 | 883 | 836 |
| 1-Heptanol | 142.8 | 858 | 804 |
| 1-Octanol | 158.5 | 851 | 783 |
| 1-Nonanol | 175 | 846 | 752 |
| 1-Decanol | 191.5 | 823 | 731 |

a Vi , molar volume;  isobaric thermal expansion coefficient; , isothermal compressibility.

Table S3. Densities ρ for Binary mixtures Aniline (AN) with 1-alkanol at T = 298.15 K and pressure p = 0.1 MPa a.

| AN(1) + 1-pentanol (2) | AN (1) + 1-hexanol (2) | AN (1) + 1-heptanol (2) | AN (1) + 1-octanol (2) |
| --- | --- | --- | --- |
| x1 |  | x1 |  | x1 |  | x1 |  |
| 0 0.0814 0.1597 0.2397 0.3497 0.4391 0.5598 0.6506 0.7406 0.8493 0.9403 1 | 0.8108 0.8256 0.8400 0.8552 0.8767 0.8947 0.9197 0.9387 0.9581 0.9821 1.0028 1.0167 | 0 0.0804 0.1599 0.2402 0.3508 0.4405 0.5598 0.6495 0.7393 0.8504 0.9396 1 | 0.8151 0.8274 0.8400 0.8534 0.8730 0.8897 0.9134 0.9322 0.9520 0.9782 1.0006 1.0167 | 0 0.0810 0.1603 0.2404 0.3511 0.4404 0.5593 0.6501 0.7400 0.8500 0.9407 1 | 0.8187 0.8294 0.8405 0.8524 0.8701 0.8856 0.9082 0.9269 0.9471 0.9743 0.9991 1.0167 | 0 0.0806 0.1597 0.2395 0.3506 0.4410 0.5609 0.6501 0.7410 0.8503 0.9406 1 | 0.8214 0.8306 0.8404 0.8510 0.8672 0.8817 0.9032 0.9214 0.9421 0.9704 0.9972 1.0167 |

a Standard uncertainties are u(T) = 0.02 K, u(x) = 0.001, u(p) = 10 kPa, expanded uncertainty for density is U(ρ) = 0.001 g·cm-3

| AN (1) + 1-nonanol (2) | AN (1) + 1-decanol (2) |
| --- | --- |
| x1 |  | x1 |  |
| 0 0.0803 0.1595 0.2396 0.3507 0.4404 0.5600 0.6493 0.7397 0.8496 0.9401 1 | 0.8240 0.8320 0.8407 0.8503 0.8651 0.8785 0.8991 0.9169 0.9375 0.9668 0.9953 1.0167 | 0 0.0796 0.1587 0.2381 0.3494 0.4401 0.5605 0.6495 0.7401 0.8504 0.9405 1 | 0.8261 0.8331 0.8408 0.8493 0.8629 0.8757 0.8954 0.9128 0.9335 0.9637 0.9936 1.0167 |

Table S3.  Continued

Table S4: Coefficients of preferential solvation,  and excess molar volumes  for binary mixtures

| Aniline(1) + 1-Pentanol (2) |
| --- |
| x1 |  |  | -0.061 -0.094 -0.141 -0.197 -0.235 -0.254 -0.226 -0.184 -0.121 -0.051 |
| 0.0814 0.1597 0.2397 0.3497 0.4391 0.5598 0.6506 0.7406 0.8493 0.9403 | 8.3 19.3 31.7 41.8 47 50.4 54.2 55 42.6 17.2 | -3.7 -11.4 -16.9 -22.6 -29 -36 -43.1 -48 -39.7 -16.6 |  |
| Aniline(1) + 1-Hexanol (2) |
| 0.0804 0.1599 0.2402 0.3508 0.4405 0.5598 0.6495 0.7393 0.8504 0.9396 | 4.5 12 22.5 33.7 38.8 42.2 45.3 47.1 37 14.8 | -5.4 -13.3 -16.2 -23.6 -29.5 -35.7 -40.9 -44.7 -37.2 -15.3 | -0.026 -0.043 -0.068 -0.103 -0.124 -0.142 -0.128 -0.097 -0.062 -0.021 |
| Aniline(1) + 1-Heptanol (2) |
| x1 |  |  | -0.004 -0.009 -0.013 -0.021 -0.031 -0.038 -0.031 -0.021 -0.009 -0.004 |
| 0.0810 0.1603 0.2404 0.3511 0.4404 0.5593 0.6501 0.7400 0.8500 0.9407 | 1.1 5.8 14.4 25.3 30.4 32.6 35.7 37.5 31.4 11.9 | -7.7 -16.7 -17.2 -25.4 -30.8 -34.7 -39.3 -41.5 -35.5 -14 |  |
| Aniline(1) + 1-Octanol (2) |
| 0.0806 0.1597 0.2395 0.3506 0.4410 0.5609 0.6501 0.7410 0.8503 0.9406 | -6.3 -11.9 -17 -22.4 -28.1 -38.2 -50.7 -57.7 -44.6 -15.5 | -12.9 -23.1 -25.1 -21.4 -18 -12.3 1.1 16.1 19.3 7.4 | 0.031 0.056 0.081 0.103 0.124 0.147 0.137 0.115 0.073 0.026 |

| Aniline(1) + 1-Nonanol (2) |
| --- |
| x1 |  |  |  |
| 0.0803 0.1595 0.2396 0.3507 0.4404 0.56 0.6493 0.7397 0.8496 0.9401 | -8.1 -15.9 -23 -31.1 -39.1 -53.3 -67.4 -77.8 -61.7 -23.9 | -16.9 -28.6 -29.9 -23.7 -16.5 -7.5 6.8 24.2 28.1 12.4 | 0.077 0.132 0.184 0.226 0.261 0.276 0.251 0.211 0.128 0.051 |
| Aniline(1) + 1-Decanol (2) |
| 0.0796 0.1587 0.2381 0.3494 0.4401 0.5605 0.6495 0.7401 0.8504 0.9405 | -10.1 -19.3 -28.6 -40.3 -50 -72.1 -91.9 -101.3 -77.7 -30.2 | -22.8 -39 -38.3 -27 -18.5 -5.6 12.8 31.4 33.2 15.4 | 0.128 0.221 0.312 0.385 0.421 0.436 0.389 0.316 0.197 0.085 |